Attachment L

FUGITIVE EMISSIONS FROM UNPAVED HAULROADS

UNPAVED HAULROADS (including all equipment traffic involved in process, haul trucks, endloaders, etc.)

|  |  | PM | PM-10 |
| --- | --- | --- | --- |
| k = | Particle size multiplier | 0.80 | 0.36 |
| s = | Silt content of road surface material (%) |  |  |
| p = | Number of days per year with precipitation >0.01 in. |  |  |
| Item Number | Description | Number of Wheels | Mean Vehicle Weight (tons) | Mean Vehicle Speed (mph) | Miles per Trip | Maximum Trips per Hour | Maximum Trips per Year | Control Device ID Number | Control Efficiency (%) |
| 1 |  |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |  |
| Source: AP-42 Fifth Edition – 13.2.2 Unpaved Roads E = k × 5.9 × (s ÷ 12) × (S ÷ 30) × (W ÷ 3)0.7 × (w ÷ 4)0.5 × ((365 – p) ÷ 365) = lb/Vehicle Mile Traveled (VMT) Where: |
|  |  | PM | PM-10 |
| k = | Particle size multiplier | 0.80 | 0.36 |
| s = | Silt content of road surface material (%) |  |  |
| S = | Mean vehicle speed (mph) |  |  |
| W = | Mean vehicle weight (tons) |  |  |
| w = | Mean number of wheels per vehicle |  |  |
| p = | Number of days per year with precipitation >0.01 in. |  |  |
| For lb/hr: [lb ÷ VMT] × [VMT ÷ trip] × [Trips ÷ Hour] = lb/hr For TPY: [lb ÷ VMT] × [VMT ÷ trip] × [Trips ÷ Hour] × [Ton ÷ 2000 lb] = Tons/year |
| SUMMARY OF UNPAVED HAULROAD EMISSIONS |
| Item No. | PM | PM-10 |
|  | Uncontrolled | Controlled | Uncontrolled | Controlled |
|  | lb/hr | TPY | lb/hr | TPY | lb/hr | TPY | lb/hr | TPY |
| 1 |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |
| TOTALS |  |  |  |  |  |  |  |  |

FUGITIVE EMISSIONS FROM PAVED HAULROADS

INDUSTRIAL PAVED HAULROADS (including all equipment traffic involved in process, haul trucks, endloaders, etc.)

| I = | Industrial augmentation factor (dimensionless) |  |
| --- | --- | --- |
| n = | Number of traffic lanes |  |
| s = | Surface material silt content (%) |  |
| L = | Surface dust loading (lb/mile) |  |
| Item Number | Description | Mean Vehicle Weight (tons) | Miles per Trip | Maximum Trips per Hour | Maximum Trips per Year | Control Device ID Number | Control Efficiency (%) |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |
| Source: AP-42 Fifth Edition – 11.2.6 Industrial Paved Roads E = 0.077 × I × (4 ÷ n) × (s ÷ 10) × (L ÷ 1000) × (W ÷ 3)0.7 = lb/Vehicle Mile Traveled (VMT) Where: |
| I = | Industrial augmentation factor (dimensionless) |  |
| n = | Number of traffic lanes |  |
| s = | Surface meterial silt content (%) |  |
| L = | Surface dust loading (lb/mile) |  |
| W = | Average vehicle weight (tons) |  |
| For lb/hr: [lb ÷ VMT] × [VMT ÷ trip] × [Trips ÷ Hour] = lb/hr For TPY: [lb ÷ VMT] × [VMT ÷ trip] × [Trips ÷ Hour] × [Ton ÷ 2000 lb] = Tons/year |
| SUMMARY OF PAVED HAULROAD EMISSIONS |
| Item No. | Uncontrolled | Controlled |
|  | lb/hr | TPY | lb/hr | TPY |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| TOTALS |  |  |  |  |