West Virginia Department of Environmental Protection

# Division of Air Quality

Fact Sheet

For Final Renewal Permitting Action Under 45CSR30 and

## Title V of the Clean Air Act

Permit Number:  R30-03900007-2015

Application Received:  May 1, 2015*

Plant Identification Number:  03900007

Permittee:  Bayer CropScience

Facility Name:  Institute Plant

Business Unit:  Emergency Services (Group 1A of 8)

Facility Name:  Institute Site

Mailing Address:  P.O. Box 1005

Institute, WV 25112

* Submitted as R30-03900007-2015 (Group 1 of 8)

Physical Location:		Institute, Kanawha County, West Virginia

UTM Coordinates:		432.00 km Easting   •  4,284.31 km Northing   •   Zone 17

Directions:	The facility is located west of Institute, WV, adjacent to State Route 25  and West Virginia State University

Facility Description

Bayer CropScience plans on selling part of this unit to the Union Carbide Corporation’s Institute Plant (03900005) over the course of two different dates.  In order to facilitate the sell, the Permittee will split the Group 1 of 8 Title V Permit as follows:

Group 1 of 8 – Powerhouse/Laboratory (will remain with Bayer)

Group 1A of 8 – Emergency Services (will be sold to Union Carbide)

Group 1B of 8 – Wastewater Treatment Unit and Maintenance (will be sold to Union Carbide)

Group 1A of 8 includes an emergency generator (EG-1), EG-1 Fuel Tank (T-EG), three Fire Pump Storage Tanks (T-699, T-154, and T-155), and three Fire Water Pumps (P-302, P-1019, and P-1020).

Emissions Summary

| Plantwide Emissions Summary [Tons per Year] |
| --- |
| Regulated Pollutants | Potential Emissions For Emergency Services Equipment | 2013 Actual Emissions (Facility Wide) |
| Carbon Monoxide (CO) | 1.4 | 268.30 |
| Nitrogen Oxides (NOX) | 6.2 | 1,344.43 |
| Particulate Matter (PM2.5) | 0.006 | 10.36 |
| Particulate Matter (PM10) | 0.22 | 23.31 |
| Total Particulate Matter (TSP) | 0.96 | 80.51 |
| Sulfur Dioxide (SO2) | 0.25 | 1,299 |
| Volatile Organic Compounds (VOC) | 0.25 | 8.76 |
| PM10 is a component of TSP. |
| Hazardous Air Pollutants | Potential Emissions For Emergency Services Equipment | 2013 Actual Emissions (Facility Wide) |
| Total HAPs | < 0.1 | 131 |
| Some of the above HAPs may be counted as PM or VOCs. |

Title V Program Applicability Basis

Due to the facility-wide potential to emit over 100 tons per year of criteria pollutants, over 10 tons per year of an individual HAP, and over 10 tons per year for an individual HAP and 25 tons per year aggregate HAPs, Bayer CropScience’s Institute Plant is required to have an operating permit pursuant to Title V of the Federal Clean Air Act as amended and 45CSR30.

Legal and Factual Basis for Permit Conditions

The State and Federally-enforceable conditions of the Title V Operating Permits are based upon the requirements of the State of West Virginia Operating Permit Rule 45CSR30 for the purposes of Title V of the Federal Clean Air Act and the underlying applicable requirements in other state and federal rules.

This facility has been found to be subject to the following applicable rules:

Federal and State:	45CSR6				Open burning prohibited.

45CSR11			Standby plans for emergency episodes.

45CSR13		Permits for construction, modification, relocation, and operation of stationary sources

45CSR16		Standards of performance for new stationary sources

WV Code § 22-5-4 (a) (14)	The Secretary can request any pertinent information such as annual emission inventory reporting.

45CSR30			Operating permit requirement.

45CSR34			Emission standards for HAP’s

40 C.F.R. 60, Subpart IIII		Standards of performance for stationary compression ignition internal combustion engines

40 C.F.R. Part 61			Asbestos inspection and removal

40 C.F.R. 63, Subpart ZZZZ	NESHAP for stationary reciprocating internal combustion engines

40 C.F.R. Part 82, Subpart F	Ozone depleting substances

State Only:		45CSR4				No objectionable odors.

Each State and Federally-enforceable condition of the Title V Operating Permit references the specific relevant requirements of 45CSR30 or the applicable requirement upon which it is based.  Any condition of the Title V permit that is enforceable by the State but is not Federally-enforceable is identified in the Title V permit as such.

The Secretary's authority to require standards under 40 C.F.R. Part 60 (NSPS), 40 C.F.R. Part 61 (NESHAPs), and 40 C.F.R. Part 63 (NESHAPs MACT) is provided in West Virginia Code §§ 22-5-1 et seq., 45CSR16, 45CSR34 and 45CSR30.

### Active Permits/Consent Orders

| Permit or Consent Order Number | Date of Issuance | Permit Determinations or Amendments That Affect the Permit (if any) |
| --- | --- | --- |
| G60-C023 | 11/19/2010 |  |
| G60-C | 5/21/2009 |  |

Conditions from this facility's Rule 13 permit(s) governing construction-related specifications and timing requirements will not be included in the Title V Operating Permit but will remain independently enforceable under the applicable Rule 13 permit(s).  All other conditions from this facility's Rule 13 permit(s) governing the source's operation and compliance have been incorporated into this Title V permit in accordance with the "General Requirement Comparison Table," which may be downloaded from DAQ's website.

### Determinations and Justifications

The Union Carbide Corporation Institute Plant intends on purchasing assets owned by the Emergency Services Section of Bayer CropScience Institute Plant.  The Bayer CropScience Group 1 of 8 plant will be broken up into Group 1 of 8 (Powerhouse/Laboratory), Group 1A of 8 (Emergency Services), and Group 1B of 8 (Wastewater Treatment Unit and Maintenance). The units transferred to this Group 1A of 8 Title V Permit include an Emergency Generator (EG-1), #2 Fuel Oil Tank (T-EG), #2 Fire Water Pump (P-302), #3 Fire Water Pump (P-1019), and #4 Fire Water Pump (P-1020), #2 Fire Water Pump Diesel Fuel Storage Tank (T-699), #3/#4 Fire Water Pump Diesel Fuel Storage Tank (T-154), and #3/#4 Fire Water Pump Diesel Fuel Storage Tank (T-155).  Bayer CropScience submitted a renewal for R30-03900007-2015 (Group 1 of 8) on May 1, 2015.  The applicable units and requirements are being transferred to this Title V Permit.

The Emergency Generator (EG-1) is subject to 40CFR60, Subpart IIII and 40CFR63, Subpart ZZZZ.  Per 40 CFR§63.6590(c)(6), a new emergency RICE with a site rating of less than 500 hp located at a major source of HAP’s must meet the requirements of 40CFR63, Subpart ZZZZ by meeting the requirements of 40CFR60 Subpart IIII.  The requirements for EG-1 and EG-1 Fuel Tank (T-EG) are contained in R13 General Permit Registration G60-C023 and General Permit G60-C.  The requirement is given in Condition 4.1.1 and the General Permit requirements are provided in Attachments A and B.  The emission unit ID and Emission Point ID for the EG-1 Fuel Tank have been changed from “6392N54277” and “6392N54277” to “T-EG” and “E-TEG”, respectively.

The diesel fueled Fire Water Pumps (P-302, P-1019, and P-1020) are subject to the existing Stationary Rice (the pumps were constructed before June 12, 2006) requirements of 40CFR63, Subpart ZZZZ.

Condition 5.1.1 requires oil changes and inspection of the air cleaner, and hoses and belts.  Condition 5.1.2 requires the Permittee to operate and maintain the pump engines in a manner consistent with safety and good air pollution control practices.  Condition 5.1.3 requires the Permittee to operate and maintain the pump engines according to the manufacturer’s instructions or to develop their own maintenance plan.  Condition 5.1.4 requires the Permittee to have a non-resettable hour meter installed on the pump engines.  Condition 5.1.5 allows the Permittee to perform an oil analysis to possibly extend the specified oil change requirements.  Condition 5.1.6 limits engines’ hours for maintenance and non-emergency situations.  Condition 5.1.7 requires the Permittee to be in compliance with all requirements of 40CFR63, Subpart ZZZZ.  Condition 5.4.1 requires the Permittee to keep records of any maintenance conducted on the pump engines.  Condition 5.4.2 requires the Permittee to keep records of the hours of operation the pump engines were used for emergency and non-emergency operation.  Condition 5.5.1 requires the Permittee to report any instance that it did not meet the requirements of Condition 5.1.1 and to report it as required by condition 5.5.3.  Condition 5.5.2 requires the Permittee to report each instance they did not meet the general provisions of Subpart ZZZZ for the pump engines.  Condition 5.5.3 requires all deviations for the pump engines be reported in the semiannual monitoring report.  Condition 5.5.4 specifies annual reporting requirements including engine information and usage.

Non-Applicability Determinations

The following requirements have been determined not to be applicable to the subject facility due to the following:

40CFR60, Subpart IIII

The Fire Water Pumps (P-302, P-1019, and P-1020) were constructed before the applicability date of July 11, 2005 for 40CFR60, Subpart IIII.

Request for Variances or Alternatives

None

Insignificant Activities

Insignificant emission unit(s) and activities are identified in the Title V application.

Comment Period

Beginning Date:	June 15, 2015

Ending Date:	July 15, 2015

Point of Contact

All written comments should be addressed to the following individual and office:

Mike Egnor

West Virginia Department of Environmental Protection

Division of Air Quality

601 57th Street SE

Charleston, WV  25304

Phone:  304/926-0499 ext. 1208   •   Fax:  304/926-0478

michael.egnor@wv.gov

Procedure for Requesting Public Hearing

During the public comment period, any interested person may submit written comments on the draft permit and may request a public hearing, if no public hearing has already been scheduled.  A request for public hearing shall be in writing and shall state the nature of the issues proposed to be raised in the hearing.  The Secretary shall grant such a request for a hearing if he/she concludes that a public hearing is appropriate.  Any public hearing shall be held in the general area in which the facility is located.

Response to Comments (Statement of Basis)

Response to EPA comments (Theresa Horgan, July 22, 2015, July 29, 2015, July 30, 2015):

Section 4 of the Permit now lists the specific requirements for Emergency Generator (EG-1) from the General Permit G60-C.

The General Permit G60-C has been added directly to the Title V Permit under Attachment B and the Permit has been renumbered accordingly.

It has been determined that the emergency engine EG-1 is certified and does not use #2 fuel oil or recycled oil as fuel.  It only uses diesel as fuel.  The design capacity of the emergency engine EG-1 in the equipment table has been corrected from 270 to 470 bhp.  “1.8 liters/cylinder displacement Diesel Fuel” has been added to the design capacity.  The description of the emergency engine fuel tank T-EG has been changed from “#2 Fuel Oil Tank” to “EG-1 Fuel Tank”.  Note that this is still the same tank listed as #2 Fuel Oil Tank in the General Permit G60-C023.

A blank line was added to separate Condition 5.1.7 from Section 5.2.

The current language of 40CFR60, Subpart ZZZZ allowed backup generators to operate up to 100 hours per year without emissions controls.  A federal appeals court (Del. Dep’t of Natural Res. And Envtl. Control v. EPA, D.C. Cir., No. 13-1093, amended opinion filed, 7/21/15) struck down the 100-hour exemption and remanded it back to the EPA for further consideration.  As it appears that this requirement will change, Condition 5.1.6 was revised to remove specific language and instead reference that the engine is subject to 40 C.F.R. §63.6640(f).