| Project: |  | Time: |  |
| --- | --- | --- | --- |
| Location: |  | Inspector: |  |
| Date: |  | Phone: |  |
| Signature: |  |  |
| Maintenance Item |  | Satisfactory Unsatisfactory | Comments |
| 1. Debris Cleanout (Monthly) |  |  |  |  |  |  |
| * Contributing areas clean of litter and vegetative debris |  |  |  |
| * Forebays and SW Structures clean of litter and vegetative debris |  |  |  |
| 2. Vegetation (Monthly) |  |  |  |  |  |  |
| * Undesirable vegetation removed |  |  |  |  |
| * Grass height less than 6 inches |  |  |  |  |
| * No evidence of erosion |  |  |  |  |
| 3. Check Dams/Energy Dissipators/Sumps (Annual, After Major Storms) |
| * No evidence of sediment buildup |  |  |  |  |
| * Sumps should not be more than 50% |  |  |  |
| full of sediment |  |  |  |  |  |
| * No evidence of erosion at |  |  |  |  |
| downstream toe of drop structure |  |  |  |  |
| 4. Dewatering (Monthly, If Designed) |  |  |  |  |
| * Dewaters between storms within 72 hours |  |  |
|  | (If Designed) |  |  |  |  |
| * No evidence of standing water |  |  |  |  |
| 5. Sediment Deposition (Annual) |  |  |  |  |  |
| * Pretreatment areas clean of |  |  |  |  |
| sediments |  |  |  |  |  |
| * Contributing drainage area stabilized |  |  |
| and clear of erosion |  |  |  |  |  |
| * Overflow window and bypass clean and clear |  |  |  |
| 6. Outlet/Overflow Spillway (Annual, After Major Storms |  |  |
| * Good condition, no need for repair |  |  |  |  |
| * No evidence of erosion |  |  |  |  |
| * No evidence of any blockages |  |  |  |  |

| Maintenance Item | Satisfactory | Unsatisfactory | Comments |
| --- | --- | --- | --- |
| 7. Integrity of Filter Bed (Annual) |  |  |  |
| * Filter bed not blocked |  |  |  |  |
| 8. Oil and Grease (Monthly) |  |  |  |
| * No evidence of surface clogging |  |  |  |  |
| * Activities in drainage area minimize |  |  |
| oil and grease entry |  |  |  |  |  |
| *Oil/ Water Separator working according |  |  |  |
| to Manufacturers specs. |  |  |  |  |
| 9. Sediment Traps and Forebays (Monthly) |  |  |
| *Water holding chambers at normal pool |  |  |  |
| * No evidence of leakage |  |  |  |  |
| * Obviously trapping sediment |  |  |  |  |
| * Greater than 50% storage volume remaining |  |  |  |
| 10. Aggregate Repairs (Annual) |  |  |  |
| * Surface of aggregate clean |  |  |  |
| * Replacement of stone |  |  |  |  |
| 11. Embankment and emergency spillway (Annual, After Major Storms) |
| * Vegetation and ground cover adequate |  |  |  |
| * Embankment erosion |  |  |  |
| * Animal burrows |  |  |  |
| * Unauthorized planting |  |  |  |
| * Cracking, bulging, or sliding of embankment |  |  |  |
| * Pond, toe & chimney drains clear and functioning |  |  |  |
| * Slope protection or riprap failure |  |  |  |  |
| * Vertical/horizontal alignment of top of dam “As- |  |  |
| Built” |  |  |  |  |  |  |
| * Emergency spillway clear of obstructions and |  |  |
| debris |  |  |  |  |  |  |
| 12. Other |  |  |  |  |  |
| * Complaints from residents |  |  |  |
| * Aesthetics |  |  |  |
| * Graffiti removal needed |  |  |  |
| * Grass growing required |  |  |  |
| * Conditions of maintenance access routes. |  |  |  |
| * Signs of hydrocarbon build-up |  |  |  |
| * Any public hazards (specify) |  |  |  |
| * Sinkholes |  |  |  |
| * Liners maintained and operating in accordance with manufacturers specifications |  |  |  |